## Slide 1: Logic Circuit Design Laboratory
Week 7 – Introduction to Verilog
Yoonmyung Lee
yoonmyung@skku.edu
Dept. of Semiconductor Systems Engineering
Sungkyunkwan University

## Slide 2
1.1 H/W Development Flow
1.2 Integration in System Design
1.3 FPGA
1. FPGA

## Slide 3: 1.1. H/W Development Flow
Program
Simulation
ASIC
Program
Simulation
FPGA
ASIC
Expensive

## Slide 4: 1.2 Integration in System Design
Integration of functions
Time
Processor
FPGA
I/O
Memory
Embedded Software Tools
Logic Design Tools
Processor
FPGA
+Memory+IP+I/O
Embedded Software Tools
Logic Design Tools
Processor+FPGA
+Memory
+IP
+I/O
Embedded Software Tools
Logic Design Tools

## Slide 5: 1.3 FPGA
A | B | C | D | Y
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0
0
1
1
1
1
0
.
.
.
A
B
C
D
MUX
Y
FPGA : Field Programmable Gate Array

## Slide 6: 1.3 FPGA
DFF
1
1
0
0
.
.
.
4
1
1
0
0
.
.
.
4
LUT (lookup table)
1
1
0
0
.
.
.
4
DFF
MUX
Slice (LUT + DFF + MUX)

## Slide 7: 1.3 FPGA
CLB: Configurable Logic Block
Virtex2  CLB = 2 x Slice
Spartan3  CLB = 4 x Slice

## Slide 8: 1.3 FPGA

## Slide 9: 1.3 FPGA

## Slide 10: 1.3 FPGA

## Slide 11
2.1 HDL
2.2 VHDL
2.3 Verilog HDL
2. HDL
Notes: 11

## Slide 12: 2.1 HDL
HDL
  - Hardware Description Language
Background
  - Hardware design method has evolved as S/W languages evolved Fortran, Cobel,
  Pascal, C, etc.
  - Good old days, logic circuit was designed by connecting elementary gates
  - As complexity of logic circuits explosively increases, language-based design
  technology was strongly desired. Verification is also an important part of design
  ➔ Birth of HDL
  - In 1983, Gateway Design Automation introduced Verilog HDL
  - Motivated by Verilog HDL, contractors of DARPA(Defense Advanced Research
  Projects Agency) developed VHDL
Notes: 제가 VHDL대해 강의 할건데요. VHDL는

## Slide 13: 2.2 VHDL
VHDL
  - VHSIC Hardware Description Language
  - VHSIC : Very High Speed Integrated Circuit
Background
  - DARPA suggested a standard logic design tool (Intermetrics, IBM, TI participated)
  - Adopted as IEEE-1076 standard, July 1987
  - Design process is performed based on the Behavioral Modeling
  - VHDL had proliferated into industrial and defense areas under governmental
  support
  - A new version of VHDL in waiting for IEEE standard approval. New VHDL has
  PSL and IP protection features.

## Slide 14: 2.3 Verilog HDL
Verilog HDL (또는 그냥 Verilog)
  - Verilog Hardware Description Language
Background
  - Language based on simulation
  - Evolved from industrial standard to IEEE 1364-1995 in 1995
  - In 2001, drastic upgrade as IEEE 1364-2001
  - IEEE1364-2005 is registered by combining System Verilog(IEEE-1800) and
  Verilog(IEEE-1364-2001).
  - Biggest merit is that different level of abstraction can be used in a single circuit
  model. (Switch, Gate, RTL, Behavioral)
Notes: 14

## Slide 15
3. Verilog
3.1 Verilog Grammar
3.2 Verilog Structure
3.3 Verilog Operator
3.4 Verilog example – Half Adder

## Slide 16: 3.1 Verilog Grammar
Rules
  - Verilog은 대소문자 구별
  - 주석 처리 시 “//” 로 처리
  - 첫 번째 문자는 영문으로 시작(숫자나 기호로 시작 불가능)
  - Reserved Keyword는 변수로 사용 할 수 없음

## Slide 17: 3.1 Verilog Grammar
Reserved Keyword
  - Verilog 내부에서 구문 구분을 위해 미리 지정된 문자열 변수로 사용 할 수 없음

## Slide 18: 3.2 Verilog Structure – Module
I/O Type | Description
input | Input signals
output | Output signals
inout | Bidirectional signals
module fulladd4(sum, c_out, a, b, c_in, d);
// 포트 선언 시작 부분
output [3:0] sum;
output c_out;
input [3:0] a, b;
input c_in;
inout d;
// 포트 선언 끝부분
…
<모듈내용>
…
end module

## Slide 19
3.2 Verilog Structure – Data Types
Nets
  - 게이트 또는 모듈 사이의 연결을 나타내며 신호가 저장되지 않음
  - Net 값이 변할 때 자동으로 Net에 새로운 값이 전달
  - 크기를 정하는 벡터를 지정하지 않으면 1bit net
Registers
  - Data를 저장하기 위한 변수
  - Net 와는 달리 새로운 값이 할당될 때 까지는 현재 값을 유지
wire a; // net a를 정의
wire b, c; // net b, c를 정의
wire d = 1’b0; // net d는 논리값 0으로 선언
reg A; // 1 bit 레지스터 A
reg [5:0] A, B; // 6 bit 레지스터 A, N
integer A; // 32 bit 정수 A
integer A, B; // 32 bit 정수 A,B

## Slide 20: 3.2 Verilog Structure – Always 문
@ 안의 event/signal 의 값들 중 하나라도 변화하면, 쓰여진 statement 가 순서대로 처리되며, 마지막 statement 까지 실행이 끝나면 처음으로 돌아가서, 다음의 event/signal 신호가 변화될 때까지 기다린다.
always문의 예
always @ (event/signal or … or event/signal)
begin
순차적인 assign문
if, case 문 등
loop, function,
task call 등
end
계속해서 순차적으로 실행
블록문이 없는 경우는 한 문장만 실행

## Slide 21: 3.2 Verilog Structure – Blocking Assignment
Initial | A=5; B=3; C=10; D=2; | 
Block | wire [3:0] A, B, C, D; always @(posedge CLK) begin C=B; B=A; A=D; end | wire [3:0] A, B, C, D; always @(posedge CLK) begin A=D; C=B; B=A; end
Result | A=2; B=5; C=3; D=2; | A=2; B=2; C=3; D=2; (A=D affects B=A)

## Slide 22: 3.2 Verilog Structure – Non Blocking Assignment
Initial | A=5; B=3; C=10; D=2; | 
Block | wire [3:0] A, B, C, D; always @(posedge CLK) begin C<=B; B<=A; A<=D; end | wire [3:0] A, B, C, D; always @(posedge CLK) begin A<=D; C<=B; B<=A; end
Result | A=2; B=5; C=3; D=2; | A=2; B=5; C=3; D=2;

## Slide 23: 3.2 Verilog Structure - BLOCKING vs NON BLOCKING
1
a
b
c
“
”
a
b
c
1
“
”
 | wire a, b, c; always @(posedge CLK) begin a = 1; b = a; c = b; end | wire a, b, c; always @(posedge CLK) begin a <= 1; b <= a; c <= b; end

## Slide 24: 3.3 Verilog Operator
형 태 | 기 호 | 연 산 자 역 할 | 형 식
산 술 연산자 | + - * / % | 덧 셈 뺄 셈 곱하기 나누기 나머지 | A + B A - B A * B A / B A % B
관 계 연산자 | > < >= <= == != | 크 다 작 다 크거나 같다 작거나 같다 같 다 다르다 | A > B A < B A >= B A <= B A == B A != B

## Slide 25: 3.3 Verilog Operator
형태 | 기호 | 연산자 역할 | 예
논 리 연산자 | && ¦¦ ! | 논리 and 논리 or 논리 not | A && B A ¦¦ B !A
비 트 연산자 | ~ & ¦ ^ ^~ or ~^ | 비트단위 not 비트단위 and 비트단위 or 비트단위 xor 비트단위 xnor | ~A A & B A ¦ B A ^ B A ~^ B)

## Slide 26: 3.3 Verilog Operator
형태 | 기호 | 연산자 역할 | 예
단항 비트 연산자 | & ~& ¦ ~¦ ^ ^~ or ~^ | 비트단항 and 비트단항 nand 비트단항 or 비트단항 nor 비트단항 xor 비트단항 xnor | & (0101) = 0 ~& (0101) = 1 ¦ (0101) = 1 ~¦ (0101) = 0 ^ (0101) = 0 ~^(1010) = 1
Shift 연산자 | >> << | 오른쪽으로 이동 왼쪽으로 이동 | 0011 >> 1 (결과: 0001) 1100 << 1 (결과: 1000)
그밖의 연산자 | {} {{}} ?: | 결합 연산자 중복 연산자 조건 연산자 | { A, B } { {A} } A ? B : C

## Slide 27: 3.4 Verilog Example – Half Adder

## Slide 28: 3.4 Verilog Example – Half Adder
Structural Modeling
Dataflow Modeling
Behavioral Modeling

## Slide 29: 3.4 Verilog Example – Half Adder
Testbench